## Slide 1: University of Gujrat Department of Computer Science
Course Code : CS-252
Computer Organization and Assembly Language
Lecture # 4
Registers, Memory Segmentation
Intel 8086

## Slide 2: Organization of the 8086/8088 Microprocessors
8086/8088 had a simplest structure and provided the basic instruction set for the other Intel processors

## Slide 3: History
Intel did release some 4-bit microprocessors but the first meaningful processor was Intel 8080 – an 8-bit processor
Intel introduced its 16-bit microprocessor Intel 8086 in 1978
Intel introduced its 8088 microprocessor in 1979 which has a slower clock rate than Intel 8086
IBM chose Intel 8088 for original PC because it was less expensive to build a computer around Intel 8088 than Intel 8086
IBM PC became very popular due to its open architecture and easily available information

## Slide 4: Introduction
Had a better performance than earlier processors
Assigns a 20 bit address to its memory locations, so 220 bytes of memory can be accessed.
Intel 8086 microprocessors has total fourteen 16 bit-registers which include General Data Registers, Address Registers and the Status Register

## Slide 5: Registers

## Slide 6: Intel 8086/8088 Registers

## Slide 7: Data Registers AX, BX, CX, DX
These four 16-bit registers are available to programmers for general data manipulations. (also called General Purpose Registers)
Instructions are processed faster if data is stored in registers
The high and low bytes of the data registers can be accessed separately
AH
AL
AX
16-bit
8-bit
8-bit

## Slide 8: Special Attributes of General Purpose Registers
AX (Accumulator Register)
Fastest for arithmetic operations. Some math instructions only use AX.
BX (Base Register)
This register can hold an address of a procedure or variable. BX can also perform arithmetic and data movement.
CX (Counter Register)
This register acts as a counter for repeating or looping instructions
DX (Destination/data Register)
This register has a special role in multiply and divide operations. In multiplication it holds the high 16 bits of the product. In division it holds the remainder. Its also used in I/O operations.

## Slide 9: Segment Registers
Segment registers are used as base locations for program instructions, data, and the stack.

## Slide 10: Segment Registers
CS (Code Segment)
Holds the base location of all instructions in a program
DS (Data Segment)
Holds the default base location for variables. It is used by the CPU to calculate the variable location.
SS (Stack Segment)
Contains the base location of the stack.
ES (Extra Segment)
This is an additional base location for memory variables.

## Slide 11: Segment Registers

## Slide 12: Index Registers
Index registers contain the offsets of data and instructions.

## Slide 13: Index Registers
SP (Stack Pointer)
Contains the offset from the top of the stack. The complete top of stack address is calculated using the SP and SS registers.
BP (Base Pointer)
Used to access data on stack. However, unlike SP, we can also use BP to access data in the other segments.
SI (Source Index)
Used to point to data in memory. Named because this is the index register commonly used as the source in string operations
DI (Destination Index)
Commonly used as the destination in string operations

## Slide 14: Data Pointers

## Slide 15: Stack Pointer

## Slide 16: Instruction Pointer
Contains the offset of the next instruction. The IP and CS registers combine to form the complete address

## Slide 17: Instruction Pointer

## Slide 18: Instruction Pointer

## Slide 19: Segmented Memory Model

## Slide 20: Background
In earlier processors like 8080 and 8085 the linear memory model was used to access memory
8080 and 8085 could access a total memory of 64K using the 16 lines of their address bus
Now, designing for the new processor, designers wanted to remain compatible with 8080 and 8085 however 64K was too small !
There are three logical parts of our program, the code data and the stack. These three logical parts of a program should appear as three distinct units in memory.

## Slide 22: Memory Segment
A memory segment is a block of 216 consecutive memory byte
Each segment is identified by a segment numbers
Within a segment the memory location is specified by given offset (16-bit)
A memory location is specified by
  Segment : Offset

## Slide 23: Physical Address Calculation
Segment Register
Offset Register
+
Memory
Segment

## Slide 24: Physical Address Calculation
16-bit segment
16-bit offset
20-bit segment
20-bit Physical Address
20-bit offset
0 0 0 0
+
0 0 0 0

## Slide 25: Example
Calculate physical address for
A4FB : 4872
Formula: Physical Address = Segment x 10h + offset
A 4 F B 0 h
0 4 8 7 2 h
A 9 8 2 2 h
+

## Slide 26: THE END